## Slide 1: Gait Analysis with IMU’s
Dr Matthew Patterson
Biomedical Data Scientist
Shimmer Research
March 11, 2020

## Slide 2: Motion Analysis
Motion analysis
  Kinematics
    Joint angles
    Motion capture
  Kinetics
    Ground reaction force
    Joint moments
Gait Analysis
  Broken down into the gait cycle (initial contact – mid-stance – toe-off – swing phase)
Xsens is industry leader at joint angle estimation from wearable sensors (biomechanics / film industry applications)
  Requires a sensor on each body segment (ie – sensor on the lower leg and the upper leg to get knee angle)
Step counting (easy to measure, easy to understand)

## Slide 3: Motion Analysis with IMU Technology
 | Motion Analysis | Gait Analysis | Physical Activity | Steps | Sleep
Sensors | Accel Gyro Magnetometer | Accel Gyro (?) | Accel | Accel | Accel
Sensor Location | Every body segment that you a joint angle from | L3 Shank Foot Chest (Garmin) | Wrist L3 | Wrist L3 Shank Foot | Wrist
Metrics | Joint angle | Step time Stride time Ground contact time Step length | Sedentary Light PA Moderate PA Vigorous PA | Steps | Time in bed Sleep efficiency

## Slide 4: Gait Cycle: Stride vs Step

## Slide 5: Traditional Heuristic Methods some more research recently on using ML methods

## Slide 6: Digital End-Points in Clinical Trials
Gait analysis with wearable sensors
Digital end-points in clinical trials
Can we find end points using new technologies that reduce time of clinical trails?

## Slide 7: Gait Analysis -
Foot – spatial / temporal gait parameters
  Close to ground, so good IC/TO detection
  Use zero velocity in stance to reduce integration time to get accurate velocity / distance parameters (step distance)
  Sabatini, A.M., Martelloni, C., Scapellato, S. and Cavallo, F., 2005. Assessment of walking features from foot inertial sensing. IEEE Transactions on biomedical engineering, 52(3), pp.486-494.
Shank – temporal gait parameters
  Investigated quantification of novel characteristics from IMU signal in relation to a gait characteristic that is associated with early onset knee osteoarthritis is ACL-reconstructed females
  Patterson, M.R., Delahunt, E., Sweeney, K.T. and Caulfield, B., 2014. An ambulatory method of identifying anterior cruciate ligament reconstructed gait patterns. Sensors, 14(1), pp.887-899.
  IC and TO are accurate, spatial parameters not as accurate
  Greene, B.R., McGrath, D., O’Neill, R., O’Donovan, K.J., Burns, A. and Caulfield, B., 2010. An adaptive gyroscope-based algorithm for temporal gait analysis. Medical & biological engineering & computing, 48(12), pp.1251-1260.
L3 – Temporal gait parameters (TO is OK, can get spatial, but not accurate)

## Slide 8: Novel Metrics from IMU’s
Investigate to see if novel metrics from IMU technology can be used to detect abnormal movement patterns
Lower knee adduction moment is associated with early onset knee osteoarthritis in ACL-reconstructed females, this was associated with a lower [3] value during gait trials

## Slide 9: Wrist vs L3
Wrist
  Activity / sedentary
  Sleep
L3
  Walking detection
  Quality of mobility (temporal gait parameters)
  Gait symmetry, gait variability

## Slide 10: Supervised vs Unsupervised
Supervised
  5m walking test, 6min walking test, Timed up and Go
  Most clinical / academic research on gait has been for supervised tests
  Comparable
  Diagnosable
Unsupervised
  Monitor patients as they go about their normal lives
  Detect when walking occurs
  Detect the gait metrics during walking periods
  Context of gait period can cause large changes (ie – carrying groceries, walking with friends)
  Little research done to develop standards
  Not diagnosable
  Difficult to get patients to wear sensors and wear them correctly
  Get data from the real world

## Slide 12
GaitPy
Open source Python library to analyze accelerometer data from L3

## Slide 13: Detect Gait Periods
Consistent periods of activity are searched for to find steady state walking periods

## Slide 14: Gait Period Variables
Category | Variable | Unit
gaitPeriods | start times | sec
 | end times | sec
 | start samples | sample
 | end samples | sample
 | gait period time | sec
 | average length | sec
 | max legnth | sec
 | std dev length | sec

## Slide 15: Initial Contact (IC) Identification
Based on Zijlstra & Hof, 2003
Anterior-posterior acceleration signal
‘..the peak forward acceleration preceding the change of sign (as determined by the zero-crossing method) is taken as the instant of foot contact’

## Slide 16: Left / Right IC Identification
Based on Zijlstra and Hof, 2003
Double integration of medial-lateral acceleration signal to obtain displacement
Positive going IC’s are right foot contacts, negative going IC’s are left foot contacts

## Slide 17: Step times / Stride times

## Slide 18: Gait Symmetry – Step & Stride
4 symmetry calculations based on the following work;
Patterson et al, 2010
Seadeghi et al, 2000
Plotnik et al, 2008
Zifchock et al, 2008

## Slide 20: Temporal / Symmetry Variable List
Category | Variable | Unit
 | steps | 
 | right step time | sec
 | left step time | sec
 | step time | sec
 | right stride time | sec
 | left stride time | sec
 | stride time | sec
 | stride time variance | sec^2
 | step cadence | steps/min
 | stride cadence | strides/min
 | artefacts step time | number
 | artefacts stride time | number
 | symmetry ratio step | 
 | symmetry ratio stride | 
 | symmetry index step | %
 | symmetry index stride | %
 | gait asymmetry step | 
 | gait asymmetry stride | 
 | symmetry angle step | 
 | symmetry angle stride | 

## Slide 21: Example data – Temporal Gait Parameters
Gait period | Length of each gait period (s) | Steps | Mean right step time (s) | Mean left step time (s) | Mean step time (s) | Mean right stride time (s) | Mean left stride time (s) | Mean stride time (s) | Stride time variance | Mean step cadence (steps/min) | Mean stride cadence
 | sec |  | sec | sec | sec | sec | sec | sec |  | steps/min | stride/min
1 | 32.56 | 19 | 0.783 | 0.811 | 0.797 | 1.688 | 1.685 | 1.686 | 0.0533 | 76.67 | 36.12
2 | 13.21 | 15 | 0.627 | 0.594 | 0.610 | 1.215 | 1.221 | 1.218 | 0.0054 | 98.73 | 49.42
3 | 49.24 | 55 | 0.614 | 0.628 | 0.621 | 1.258 | 1.260 | 1.259 | 0.0163 | 97.63 | 48.10
4 | 18.38 | 8 | 0.677 | 0.679 | 0.678 | 1.250 | 1.279 | 1.265 | 0.0095 | 90.05 | 47.59
5 | 63.58 | 65 | 0.662 | 0.684 | 0.673 | 1.373 | 1.352 | 1.362 | 0.0148 | 90.58 | 44.39
6 | 49.30 | 37 | 0.645 | 0.646 | 0.645 | 1.324 | 1.305 | 1.314 | 0.0177 | 94.35 | 46.07
7 | 100.20 | 98 | 0.631 | 0.622 | 0.626 | 1.252 | 1.261 | 1.256 | 0.0126 | 97.11 | 48.13
8 | 18.20 | 9 | 0.710 | 0.651 | 0.680 | 1.318 | 1.372 | 1.345 | 0.0069 | 88.75 | 44.70
9 | 451.31 | 729 | 0.596 | 0.589 | 0.592 | 1.188 | 1.186 | 1.187 | 0.0044 | 101.69 | 50.70

## Slide 22: Example data – Temporal Gait Parameters
Chart: Step Time Comparison
Mean right step time (s) | 0.7832 | 0.62663 | 0.61445 | 0.67708 | 0.66238 | 0.64453 | 0.63113 | 0.70963 | 0.59579
Mean left step time (s) | 0.81055 | 0.59407 | 0.62755 | 0.67871 | 0.68432 | 0.64603 | 0.62167 | 0.65104 | 0.58856
Chart: Stride Time Comparison
Mean right stride time (s) | 1.6875 | 1.2148 | 1.2576 | 1.25 | 1.373 | 1.3236 | 1.2518 | 1.3184 | 1.1876
Mean left stride time (s) | 1.6846 | 1.2207 | 1.2598 | 1.2793 | 1.3516 | 1.3048 | 1.2605 | 1.3721 | 1.186
Chart: Cadence Comparison
 | 76.6729 | 98.7322 | 97.6313 | 90.0477 | 90.5831 | 94.3466 | 97.1069 | 88.7534 | 101.69