## Slide 1: Accelerometer Data from NHANES 2011-2014
Rick Troiano

## Slide 2: Objectives
  NHANES 2011-2014 protocol vs 2003-2006
  Preliminary results (meta data)
  Data QC and processing
  Release plans

## Slide 3: NHANES Accelerometer Protocols
2003-2006 Protocol
Ages 6 years +
Waist worn monitor
Splash proof
  No swimming or showering
Waking hours only
  No objective sleep data
Uniaxial (vertical axis)
1-minute epoch
2011-2014 Protocol
Ages 3 years + (6+ for 2011)
Wrist worn monitor
Waterproof device
24-hour wear
  Allows measures of sleep
Triaxial (X, Y, & Z planes)
80Hz raw data + lux

## Slide 4: 2011-14 Preliminary Data

## Slide 5: NHANES Component Compliance
Over 4 years:
  >16,000 participants agreed to wear (including Youth Fitness Survey)
    ~92% of examinees ages 3 years and older
    Acceptance by age group was ~90% or greater
  >95% of devices were returned by participants

## Slide 6: Data Processing

## Slide 7: Starting point: The data
Provided data for 16,460 participants
  Device ID, age, gender, day of week
  80 Hz accelerometer sampling rate
  1 Hz light sensor (lux) sampling rate
Up to 7 full + two partial days
1.66 TB
gt3x Actigraph files

## Slide 8: Five stages
Convert data to non-proprietary format
Flag data with potential quality issues
Compute a non-proprietary motion summary
Estimate wake-wear, wake-sleep, non-wear
Merge data from separate files into manageable summary files

## Slide 9: Stage 1: Convert raw format
Convert to non-proprietary raw format (“mHealth format”)
  Raw data (csv), split by hour
  Accelerometer: timestamp, x, y, z +/- 6 g (actually +/- 6.006 g)
  Lux: timestamp, lux 0.00 – 2500.00
Expands size to 4+ TB, but simplifies use

## Slide 10: Stage 2: Quality control check
Identify anomalies (suspicious/corrupted data)
  Some just a few seconds
  Some hours
Tests incrementally added
No systematic pattern of problems isolated to a particular device or firmware version were observed

## Slide 11: Anomalies observed
“Stuck” signals
Too many spikes
Impossible signals based on gravity
Non-human oscillation
Abnormal signal pattern

## Slide 12: Complete days of data
Target: 7 full days (+ 2 partial)
Complete days of data | # participants
7 | 15,965
6 | 91
5 | 72
4 | 83
3 | 76
2 | 68
1 | 68
0 | 20

## Slide 13: Stage 3: Motion summary value
Non-proprietary, open-source Monitor-Independent Movement Summary unit (MIMS-unit)
  Interpolation
  Extrapolation
  Filtering
  Aggregation
Output minute-level summaries
Computed across ALL (inc. flagged) data
    John et al., 2019 J Meas Phys Behav 2, 268-281

## Slide 14: Stage 4: Wake/sleep/non-wear
Three pass algorithm
Pass 1:
  Trained machine learning algorithm to classify 30s windows
    Iterative Spectral Method: Use “reversed ISM”
    Experimentally improved sleep/non-wear differentiation
  Use three adjacent windows (1.5 min)
  Sometimes sleep/non-wear indistinguishable

## Slide 15: Stage 4: Wake/sleep/non-wear
Pass 2:
  Wear (< 3 min), sleep (< 10 min) and non-wear (< 10 min) are filtered
  Uses summation of confidence values across 1.5 min
Pass 3:
  Orientation changes used to flip labels from non-wear to sleep, or sleep to non-wear
Output: class per minute (or uncertain)

## Slide 16: Classification
Algorithm tuned with small labeled training/test set
    Established non-wear
    Established sleep (PSG)
    Active wear
Performs as well or better than currently accepted approaches on test set

## Slide 17: Wake-wear, sleep-wear, non-wear
Estimates must be interpreted cautiously, and will require more time to fully understand. Overall trends seem reasonable, but also many outliers.
We have already identified some possible improvements.

## Slide 18: Non-wear detection
8,902 (54%) participants have seven full days of data recorded with absolutely no non-wear detected
For rest, when non-wear detected, some could be sleep

## Slide 19: Sleep summary

## Slide 20: Data Release Plans

## Slide 21: Data Release Plans
Advanced
80hz Data
Cloud? Fresh drive
High Frequency Data
Moderate
Minute/Hour MIMS, Sleep/Wear
Website
(SAS flat file)
Intermediate Data
Basic
Daily MIMS, Sleep/Wear
Website
(SAS flat file)
Daily Summary
Release Product
Audience
Data Access

## Slide 23: Examples of anomalous data
Continuous max
Instantaneous spikes
Interval fluctuations
Samples (80 Hz)
g

## Slide 24: Anomalous data (continuous max (1 axis))
~ 20 minutes

## Slide 25: Anomalous data (multiple issues)
For anyone accustomed to looking at raw accelerometer data, portions of this look normal....
… and other parts do not

## Slide 26: Algorithm outputs (un)certainty